## Slide 1: EEE-414 Electrical Services Design
Final Project Presentation
Group-04
Group Members:
1. Md. Fahadul Islam- 1906054
2. Tasmin Khan- 1906055
3. Bokhtiar Foysol Himon- 1906056
4. Tawsif Arefin- 1906057
5. Mohammad Ismail Chowdhury- 1906058
6. Md. Hasib Ur Rashid- 1906059

## Slide 2
Building Overview
Symbols & Legends
Floor Plans (with Fittings and Fixtures)
  Floor Plan : Single Unit
  Floor Plan : Typical Floor
  Floor Plan : Ground Floor (with Substation Layout)
  Floor Plan: Basement
Conduit Layout
  Conduit Layout: Single Unit
  Conduit Layout : Typical Floor
  Conduit Layout : Ground Floor
  Conduit Layout : Basement
Emergency Conduit Layout
  Emergency Conduit Layout: Single Unit
  Emergency Conduit Layout : Typical Floor
  Emergency Conduit Layout : Ground Floor
  Emergency Conduit Layout : Basement
5. Power Socket Conduit Layout
a. Single Unit
b. Ground Floor
6. Lightning Protection System Layout
7. Earthing System Diagram
8 . SwitchBoard Connection Diagram(with Calculation)
Ground Floor
Basement
Typical Floor
Rooftop
8. Emergency SwitchBoard Connection Diagram(with Calculation)
Ground Floor
Basement
Typical Floor
8. Sub Distribution Board Diagram(with Calculation)
Ground Floor
Garage
Typical Floor
9. Emergency Sub Distribution Board Diagram(with calculation)
Ground Floor
Garage
Typical Floor
10. Load Calculation Sample
11. Reference

## Slide 3
Building Overview:
We are designing a 9-storeyed building
We have 4 units each floor
We have 3 different types of floor design:
Typical floor consisting of 4 identical units
Ground floor containing car parking, guard room, guard and caretaker residence and a substation
Basement containing car parking
Each floor contains two lifts (one main, one emergency) and two flights of stairs (one main, one emergency exit)
Lightning protection system is added to prevent damage from lightning strikes
Proper earthing system is installed

## Slide 4
Electrical Appliances Symbols and Legends:

## Slide 5
Floor Plan with Fittings and Fixtures

## Slide 6
Fittings calculation:

## Slide 7
Single Unit Floor Plan (with Fittings and Fixtures):
Area (Unit)= 992 sq ft

## Slide 8
Typical Floor Plan:
(with Fittings and Fixtures)
Two lifts- 1 main lift, 1 emergency lift
Two staircases- 1 main staircase, 1 emergency staircase during hazard
The lobby has 3 ceiling lights placed at suitable distance
The staircases have 1 ceiling light each

## Slide 9
Ground Floor Plan:
(with Fittings and Fixtures
and Substation Layout)
The ground floor has a guard room
It has a separate residence for guard and caretaker
The substation consists of-
HT meter panel room (Door locked and only accessible to grid operators). It has a window on the outside for reading the meter
HT switchgear
Transformer is surrounded by a netted boundary.
LT switchgear
Generator room with proper fittings
ATS

## Slide 10
Substation Design:
Capacity of Transformer (kVA) | Transformer Area (sq. m) | Total Substation Area (with HT, LT Panels & Transformer Room but Without Generators) (sq. m.)
1x150 | 12 | 45
1x250 | 13 | 48
2x250 | 26 | 100
1x400 | 13 | 48
2x400 | 30 | 100
3x400 | 40 | 135
2x630 | 26 | 100
3x630 | 40 | 190
2x1000 | 40 | 180
3x1000 | 45 | 220
Capacity of Generator (kW) | Area of Generator Room (sq. m.)
1x25 | 20
1x48 | 24
1x100 | 30
1x150 | 36
1x300 | 48
1x500 | 56
Transformer used- 11/0.415 kV, 315 kVA, DYN11
Transformer area= 13 sq. m
Substation Area (With HT Panel, LT Panel, Transformer Room and HT Metering Room)= 46.44 sq. m.
Generator Requirement= 13 kW
Generator Room Area= 21.73 sq. m.

## Slide 11
Basement Plan:
(With Fittings and Fixtures)
Basement has adequate space for parking
It has adequate ceiling lights at appropriate spaces

## Slide 12
Conduit Layout

## Slide 13: Conduit Schedule
Symbol | Containing Power Cable | Current Rating
C1 | 2*1.5 rm BYM + 1.5 rm BYA | 5A
C2 | 4*1.5 rm BYM + 2*1.5 rm BYA | 5A
C3 | 6*1.5 rm BYM + 3*1.5 rm BYA | 5A
C4 | 8*1.5 rm BYM + 4*1.5 rm BYA | 5A
C5 | 10*1.5 rm BYM + 5*1.5 rm BYA | 5A
C6 | 2*2.5 rm BYM + 2.5 rm BYA | 10A
C7 | 4*2.5 rm BYM + 2*2.5 rm BYA | 10A
C8 | 2*4 rm BYM + 4 rm BYA | 15A
C9 | 4*4 rm BYM + 2*4 rm BYA | 15A
C10 | 2*6 rm BYM + 6 rm BYA | 20A
C11 | 2*10 rm BYM + 10 rm BYA | 30A
C12 | 2*25 rm BYM + 16 rm BYA | 50A

## Slide 14
Conduit Layout
(Single Unit):

## Slide 15
Conduit Layout (Typical Floor):
Separate SB and SDB for lights in the lobby and staircase
Conduit from SDB of each unit and from SDB of lobby carried to MDB through electrical service shaft*
* 200 mm x 400 mm for every 1500 sq. m. floor area as per BNBC 2020

## Slide 16
Conduit Layout (Ground Floor):
Proper fittings and fixtures at the rooms in substation as per BNBC 2020
Generator and HT metering rooms have proper ventilation with windows and exhaust fans
A fan has been included in transformer room for proper ventilation
Generator room has proper clearance on all sides (> 1.0 m)
Similar clearance for transformer room

## Slide 17
Conduit Layout (Basement):

## Slide 18
Emergency Conduit Layout

## Slide 19
Emergency Conduit Layout (Single Unit):
The fittings connected to emergency line has been named with a suffix ‘E’ for quick identification
The fans connected with emergency line has been indicated by a symbol separate from fans connected with normal supply from grid.

## Slide 20
Emergency Conduit Layout
(Typical Floor):
One of the lights in the lobby and both of the lights in the staircase have been connected to the emergency line
Conduit from ESDB of each unit and ESDB of lobby goes to EMDB through electrical service shaft

## Slide 21
Emergency Conduit Layout
(Ground Floor):

## Slide 22
Emergency Conduit Layout
(Basement):

## Slide 23
Conduit Layout for Power Sockets

## Slide 24
Power Socket Conduit Layout (Single Unit):
C10 and C11 conduits (as mentioned in the conduit list) has been used for P and Q sockets since they have higher current ratings.

## Slide 25
Power Socket Conduit Layout
(Ground Floor):

## Slide 26
Lightning Protection System Layout

## Slide 27
Lightning Protection System:
The distance has been fixed and the height of the conductors have been determined using the rolling sphere method.
R for rolling sphere method has been considered as 45 m
Number of down conductors have been calculated by taking the entire area in sq. m and putting 1 down conductor for the first 80 sq. m and 1 down conductor for every 100 sq. m after the first conductor.
Total number of down conductors= 5
The lightning rods have been expanded in the figure for visual identification
Separate SB and SDB for fittings in the lobby for the roof

## Slide 28
Earthing System Diagram:

## Slide 29
Earthing System:
An earthing pit has been used with each down conductor
Multiple earth electrodes may have to be installed for earth resistance < 1 Ohm
2 earthing pits have been placed at HT and LT sides of transformer for safety
Minimum Cu rod diameter= 12.5 mm
Minimum length= 3.33 m

## Slide 30
Switchboard Diagrams:

## Slide 31
Switch Board(Each Unit):

## Slide 32
Switch Board(Ground Floor):

## Slide 33
Switch Board(Basement):

## Slide 34
Switch Board(Lobby and Roof):

## Slide 35
Emergency Switch Board(Each Unit):

## Slide 36
Emergency Switch Board(Ground):

## Slide 37
Emergency Switch Board(Basement and Lobby):

## Slide 38
Distribution Board Diagrams:

## Slide 39
SDB Diagram (Each Unit):

## Slide 40
SDB Diagram (Ground Floor and Basement):

## Slide 41
SDB Diagram (Lobby and Roof):

## Slide 42
ESDB Diagram (Each Unit, Ground):

## Slide 43
ESDB Diagram (Basement and Lobby):

## Slide 44
EMDB Diagram:

## Slide 45
MDB Diagram:

## Slide 46
Relevant Calculations:

## Slide 47
Sample Calculation(SB Calculation _ Each Unit):

## Slide 48
Sample Calculation(SDB Calculation- Each Unit):

## Slide 49
Sample Calculation(EMDB Calculation):

## Slide 50
Sample Calculation(Generator Sizing):

## Slide 51
Sample Calculation(MDB Sizing):

## Slide 52
Sample Calculation(Transformer Rating):
(reference) PWD RATE SCHEDULE 2.1.4.6

## Slide 53
Sample Calculation(PFI Plant):

## Slide 54
References:

## Slide 55
References:
2. PWD Website : https://ss.pwd.gov.bd/sor/sordownload/2